## Slide 1: Seasonal and longitudinal nutrient limitation patterns in a watershed influenced by irrigation delivery and return flow
C Arango, S Roley, A Alexiades

## Slide 2: The Yakima Basin
Largest basin entirely within Washington
Mixed land use roughly evenly split between
Forest
Range
Agriculture
Johnson 2007

## Slide 3: Strong Precipitation Gradient
Forested headwaters up to 200” precipitation
Alluvial valleys less than 10” precipitation
WA Dept. of Commerce

## Slide 4: Highly Seasonal Precipitation
Most precipitation as winter snow
Snowmelt runoff pattern
80% of
precip

## Slide 5: Water Infrastructure
USBR
Headwater storage reservoirs capture snowmelt for summer delivery to irrigation districts
1 mil acre feet
storage

## Slide 6: Irrigation Delivery and Return Flow
Low nutrient snowmelt delivered throughout summer
Return flow has lower water quality
Yakima side channel
Irrigation return flow

## Slide 7: Irrigation Alters Seasonality of N:P Ratio
Fuhrer et al. 2004
Low NO3- snowmelt delivered to fields + sediment erosion = low N:P
NO3- -rich groundwater discharged after irrigation = high N:P
This pattern was documented in one tributary drain

## Slide 8: Does irrigation delivery affect the nutrient limitation status of stream biofilms?
We hypothesized:
1 – seasonal differences in stream water nutrient concentrations
2 – seasonal differences in nutrient limitation status for autotrophs and heterotrophs
3 – spatial differences in nutrient concentrations due to irrigation return flow dominating downstream sites…
4 – …leading to increased role of Si in GPP in downstream sites

## Slide 9: Study Sites
Arrayed longitudinally approximately equidistant along the river continuum
Upper basin generally has better water quality than lower basin

## Slide 10: Study Design
NDS deployed in 6 main stem sites
  Fully crossed treatments of N (as NO3-), P, and Si (n=80 per deployment)
Deployments in summer during irrigation delivery and in fall 2-4 weeks after irrigation
12-14 day deployment; light+dark assays in lab to measure production and respiration

## Slide 11: Results: Nutrient Concentrations
paired t-test, p=0.79
Ammonium did not vary seasonally
Below detection in 4/6 sites in summer
Upper basin
Lower basin
Lower basin had higher ammonium than the upper basin in the fall

## Slide 12: Nutrient Concentrations
paired t-test, p=0.026
Nitrate was higher in fall compared to summer
Upper basin
Lower basin
Nitrate loads increased moving downstream in summer and fall (fall shown)

## Slide 13: Nutrient Concentrations
paired t-test, p=0.19
DOC ranged from 1.2 – 9.7 mg C/L, but no seasonal difference
DOC higher in the lower basin in summer but not fall
Upper basin
Lower basin

## Slide 14: Nutrient Limitation Status of GPP
Nutrient limitation status changed in 3 sites between summer and fall
Release of N limitation in two sites
Silica became important at the downstream sites that generally have higher nutrient concentrations
N
no lim
N+P+Si
P
?
 no lim
 no lim
no lim
 no lim
 Si*
 Si
 Si*
Summer
Fall

## Slide 15: Nutrient Response to Water Chemistry
p=0.48
Production response was not related to background DIN

## Slide 16: Nutrient Limitation Status of CR
Nutrient limitation status changed in 1 site between summer and fall
Release of N limitation
Two sites could not be evaluated due to loss of control samples
N
N
no lim
P
no lim
 N
 no lim
N
 N
 no lim
 ?
 ?
Summer
Fall

## Slide 17: Nutrient Response to Water Chemistry
R2=0.37
p=0.021
Respiration response was inversely related to background DIN

## Slide 18: Conclusions
End of irrigation increased mainstem NO3- similar to what was documented in a tributary
The NO3- increase relieved N limitation of GPP and CR in some sites but not others
Silica limitation was observed in downstream sites that often have high N and P concentrations

## Slide 19: Implications
Less retention of NO3- pulsed in late fall/winter due to low light, thus increasing export
Terrestrial DOM is likely pulsed after the irrigation season too, with consequences for the DOM lability and the heterotrophic community
Silica limitation of GPP should be investigated in systems with high N and P concentrations

## Slide 20: Acknowledgements
Yakama Nation for site access
Rhenton Brimberry, Cassandra Elkins, Alifya Saify, Noelle Scofield, Allison Staten, and Sarah’s parental units all assisted in the field and in the lab
Internal funding from CWU and WSU helped make this research possible